## Slide 1
Conrad Schiff1 (Conrad.Schiff-1@nasa.gov), George Khazanov1, Barbara L. Giles1, Levon A. Avanov1,2, J.L. Burch3,V.N. Coffey4, J.C. Dorelli1, D. Gershman1,2, B. Lavraud5, T. E. Moore1, W.R. Paterson1, C.J. Pollock6,C.T.Russell7,Y. Saito8, J.-A. Sauvaud5,R.J. Strangeway7 |1NASA Goddard Space Flight Center, Greenbelt, MD, 2University of Maryland, College Park, MD, 3Southwest Research Institute, San Antonio, TX, 4NASA Marshall Space Flight Center, Huntsville, AL, 5Research Institute in Astrophysics and Planetology, Toulouse, France, 6Denali Scientific, Healy, AK, 7University of California, Los Angeles, CA, 8Institute for Space and Astronautical Science, Sagamihara, Japan
Data Analysis and Methodology
FPI electron skymaps consist of measured counts distributed over 512 cells (; 32 azimuth () 16 polar angles ()) over 32 energies [5]
Each cell has a look direction with a corresponding flow direction
Magnetic field in the instrument frame used to construct pitch angle distribution for each cell,
Considered error sources: a) Spacecraft potential, b) Instrument-generated photoelectrons, c) Poisson-noise/counting statistics
Differential Electron Flux Spectra Measured by the Magnetospheric Multiscale Mission Show Strong Field-aligned Electron Population of Ionospheric Origin
Background
The lead author would like to gratefully acknowledge the opportunity afforded by and the patience and support of George Khazanov, Barbara Giles, and Levon Avanov, and the professionalism and dedication of the MMS Flight Dynamics, FIELDs, and (especially) Fast Plasma Investigation Teams.
Results
Motivation and Context
The Magnetospheric Multiscale (MMS) fleet, launched by NASA on Mar. 13th 2015, is an elliptical, formation-flying mission whose primary purpose is studying magnetic reconnection [1]. Fitted with an array of particle and field instruments, MMS spends between 12-14 hours each orbit in its science region of interest (sROI ~ ). When the fleet is in the sROI but away from the magnetopause, there are opportunities to observe/measure secondary electron fluxes of ionospheric origin generated by precipitating magnetospheric superthermal electrons.
Precipitating superthermal electrons are one of the main mechanisms contributing to ionospheric mass escape [2]. They form an additional source of ionization via impact and generally lead to heating and subsequent upflowing.
Superthermal electron physics, as studied extensively in [3-4], identifies the importance of multiple reflections between the conjugate ionospheric footprints of closed field lines. These counterstreaming fluxes interact with the replenished population and secondary fluxes leading to distinct spectra [3]
[1] Fuselier et al. (2016), Space Science Reviews 199
[2] Moore et al. (2010), J. Geophys Research 115.
[3] Khazanov et al. (2013), J. Geophys Research 119
SM21A-2445
Conclusions & Future Work
We present experimental observations of binned pitch angle distributions and excess secondary flux between sunlit and shadowed conjugate points for 3 survey cases distributed in the magnetosphere
Each magnetic field configuration gives a unique signature that will inform the identification of the appropriate wave-particle interaction (e.g. ECH, Whistler Chorus, etc.) that scatters plasma sheet electrons into the precipitating population
Improvements in correcting for instrument-generated photoelectrons is needed to improve knowledge of low-energy electron distributions in the counter-streaming fluxes
Mar 02, 2016 600
Oct 26, 2015 0
Aug 04, 2015 538
Data analyzed during stable magnetic field conditions when the observatory sits in the magnetosphere on closed filed lines (columns 1 and 2)
Collecting data into discrete bins provides survey spectra (column 3) and excess spectra between sunlit and shadowed conjugate footprints (column 4).
[4] Khazanov et al. (2015), J. Geophys Research 120
[5] Pollock et al., (2016), Space Sci. Rev., 199
Flux Spectrum by Pitch Angle
GSM Fieldline
Trace
Magnetic Field
Excess Flux:
Sunlit - Shadowed
References
Acknowledgements